## Slide 1: Streamloading: Low Cost High Quality Video Streaming for Mobile Users
Ayaskant Rath, Sanjay Goyal, and Shivendra Panwar
MoVid’13

## Slide 2: Introduction
Cellular data traffic will grow by over 8 times in the next four years.
A user located closer to a base station experiences a higher data rate.
Data rate available to a user almost instantaneously reflects on the quality of video.
Streamloading:
  SVC
  Streaming base layer
  Downloading enhancement layers

## Slide 3: Streaming V.S. Downloading
Streaming:
  Cache short period of video data
Downloading:
  Cache as much of the video as network bandwidth allows
Streaming drawback:
  Cannot cache future chucks of video
  Video quality drops as soon as they move away from the base station

## Slide 4: Streamloading
Stream the base layer data
Download the enhancement layer data

## Slide 5: Implementation
ci : ith chunk, 0 <= i <= N
Each ci is encoded in M layers
sij : subchunk of chunk ci, si0 is base layer, 0 <= j <= M
b : buffer size in term of chunk

## Slide 6: Simulation Model
Macrocell: WiMAX
Femtocell: WiFi hotspot
Transmission Scheduling: TDMA, 2ms

## Slide 7: Video Data
Chunk length: 1.2s
Videos length: 100m → N = 5000
M = 4

## Slide 8: Results and Analyses
Average speed of 11 mph
b = 4 chunks
Streamloading service provides more than two enhancement layers of video the users on the average

## Slide 9: Results and Analyses (cont.)
66 users consuming ED videos
31 users consuming HD videos

## Slide 10: Results and Analyses (cont.)
Without fetmocell
b = 3 chunks
Only CIF video
(a) At 340 users, streamloading delivers up to two additional layers of video
(b)streamloading: more than 82% were perfect quality

## Slide 11: Conclusion
With 20 femtocells:
  Streamloading can serve more than 50% additional users with near perfect video quality
Without femtocells:
  This number is found to be as high as 35%
They proposed a novel video delivery service, streamloading:
  Streaming base layer
  Downloading enhancement layers
  In the worst case is no worse than streaming
  In the best case is as good as downloading