## Slide 1: “Can you SEE me now?” A Measurement Study of Mobile Video Calls
Chenguang Yu, Yang Xu, Bo Liu and Yong Liu
Department of Electrical and Computer Engineering
Polytechnic Institute of New York University
Brooklyn, New York, 11201
Email: fcyu03, yxu10, bliu01g@students.poly.edu, yongliu@poly.edu

## Slide 2: Introduction
Users prefer to make untethered video calls using their mobile devices instead of sitting in front of their desktop computers.
Can you SEE me now?
FaceTime, Google Plus Hangout, Skype

## Slide 3: Focus on
How they encode and decode video in real-time under tight resource constraints on mobile devices?
How they transmit the encoded video smoothly in face of various wireless network impairments?
What is their delivered video conferencing quality under different real mobile network conditions?
How different system architectures and design choices adopted by each system contribute to user-perceived video conferencing quality?

## Slide 4: Measurement
Heterogeneity and volatility of wireless networks
  A controlled network emulator
  A campus WiFi network with strong and weak signal receptions
  A cellular network of one top-three US carrier with and without user mobility
Collect extensive measurement traces at packet level and video level

## Slide 5: Findings
With a strong WiFi/Cellular connection, modern smartphones are capable of encoding, transmitting and decoding high quality video in real-time
Mobile video call quality is highly vulnerable to bursty packet losses and long packet delays, which are sporadic on wireless links with weak receptions

## Slide 6: Findings(cont.)
While FEC can be used to recover random packet losses, the inability to differentiate congestion losses from random losses can trigger vicious congestion cycle, and significantly degrade user video call experience
Conservative video rate selection and FEC redundancy schemes often lead to better video conferencing quality, compared with more aggressive schemes

## Slide 7: Findings(cont.)
End-to-end video delay is highly correlated to end-to end packet delay in Cellular networks, regardless of the signal strength

## Slide 8: Related Work

## Slide 9: Measurement Methods
Black boxes
Perform IP-level packet sniffing
Application-level information window capturing
Video-level quality analysis
2-party video calls

## Slide 10: Testbed
Overall Platform
  wireless user side ⟷ wireline user side
  Software-based network emulator
  Wireshark
  Akiyo

## Slide 11: Testbed(cont.)
Smartphone Hacks(iPhone 4s)
  Privilege escalation
    RedSn0w(jailbreak)
  Measurement tool installation
    Collect CPU and network statics
    Remotely login
  Remote phone control(via ssh)
    USB (computer)
    Set iPhone to WiFi ad-hoc mode(phone)

## Slide 12: Testbed(cont.)
Wireless network setting
  Conduct WiFi and Cellular experiments at several locations with Strong & weak signal
  Use SpeedTest to verify the actual upload throughput
  NEWT(Network Emulator for Windows Toolkit)
    Propagation delay, random packet loss, available bandwidth, ……
 | Strong | Weak
WiFi | 10mbps | 200-300kbps
Cellular | 1000kbps | 100-150kbps

## Slide 13: Information Collection
IP Packet Traces
  Packet delay, packet loss(wireshark, tcpdump)
Video Quality Logs
  Video rates, frame rates, RTT
End-to-End Video Delay Samples
  Sender side generate video frame → display on the receiver side
  Video capturing, encoding, transmission, decoding, rendering delays

## Slide 14: Information Collection(cont.)

## Slide 15: Information Collection(cont.)

## Slide 16: How Do They Work?
Architecture and protocol
System | P2P or Server | UDP or TCP | RTP | RTT
Skype | Relay server or P2P | UDP, may use TCP | No | 14ms
Google+ | Server-centric | UDP, only use TCP when UDP is blocked | Yes | 4~37ms
FaceTime | WiFi: mostly P2P Cellular: relay server | Always use UDP | Yes | 2~20ms

## Slide 17: How Do They Work?(cont.)
Video rate ranges and encoding parameters
  Google+ : layered video coding
    CPU utilization → 100%
    Consumes 40% more than others
System | Range(kbps) | Resolution | FPS
Skype | 10-620 | 480*360, 320*240 | 1-12
Google+ | 20-800 | 480*360, 240*180 | 1-15
FaceTime | 10-820 | ??*?? | 1-30

## Slide 18: How Do They Work?(cont.)
Loss Recovery
  Inject random packet losses
  Start with zero loss rate, then increase loss rate by 5% every 120 seconds
  Selectively retransmission
  Adaptive-but-aggressive FEC scheme
  Frame-based FEC scheme

## Slide 19: How Do They Work?(cont.)
Rate Control
  Start with “unlimited” bandwidth setting
  Bandwidth⟶200kbps higher than current sending rate, then Dropping the bandwidth limit by 100 kbps every 2 minutes

## Slide 20: Conferencing quality over wireless
Video conferencing quality
  Various encoding parameters, video frame size, frame rate, quantization level
  Highly sensitive to end-to-end video delays, video playback continuity and smoothness
  High rate & low delay

## Slide 21: Video conferencing quality
Voice delay
  The phone call service is more stable than the three systems
  In Cellular network, the mean voice delay of Skype is the lowest among all applications

## Slide 22: Video Quality over WiFi
Strong signal
Weak signal

## Slide 23: Video Quality over Cellular
Strong signal
Weak signal

## Slide 24: Round-Trip Video Delay On Subway

## Slide 25: Impact of Packet Losses
Match packet traces collected at the sender and the receiver side

## Slide 26: Impact of Packet Losses(cont.)

## Slide 27: Impact of Packet Delays

## Slide 28: Impact of Packet Delays(cont.)
Cross-correlation function between video delay and packet delay

## Slide 29: Conclusion
Mobile video call quality is highly vulnerable to bursty packet losses and long packet delays
While FEC can be used to recover random packet losses, the inability to differentiate congestion losses from random losses can trigger vicious congestion cycles
conservative video rate selection and FEC redundancy schemes often lead to better video conferencing quality

## Slide 30: Conclusion
end-to-end video delay is highly correlated to end-to-end packet delay in cellular networks, regardless of the signal strength
Insights obtained in this study can be used to guide the design of new solutions to deliver high-quality video calls in wireless networks