## Slide 1: Cognitive Passive Estimation of Available Bandwidth (cPEAB) in Overlapped IEEE 802.11 WiFi WLANs
Shahnaza Tursunova, Khamidulla Inoyatov and Young-Tak Kim
Dept. of Information and Communication Engineering, Graduate School, Yeungnam University Gyeongsan, Korea
Email: {sh tursunova, kinoyatov}@ynu.ac.kr, ytkim@yu.ac.kr
Network Operations and Management Symposium (NOMS), 2010 IEEE

## Slide 2: Introduction
Available bandwidth estimation  efficient network resource management、QoS-guaranteed applications
  active probing -> extra traffic load
  passive measurements -> not considering the overhead of control messages
  mathematical model -> highly dependent on the network topology
cognitive passive estimation of the available bandwidth
  the proportion of waiting and backoff delay
  packet collision probability
  Acknowledgement delay
  channel idle time compared to measurement period

## Slide 3: Cognitive Passive Estimation of Available Bandwidth
Channel usage ration considering
  possible overhead by control messaging which may occur in future
  impacts from hidden/exposed terminals
  observed channel information considering different packet size

## Slide 4: Possible Overhead by Control Messaging
Channel idle time
Measurement period
Maximum capacity
Maximum number of retransmissions
the proportion of bandwidth consumed by the DIFS and backoff mechanism

## Slide 5: Impact of Hidden/Exposed Nodes and Packet Size
data frame transmission depends on the frame size
frame size has direct impact to the packet collision rate
consider the impact from hidden/exposed terminal
Total data flow of the hidden nodes
Total data flow of the exposed nodes
data flow information is provided through IEEE 802.21 Media Independent Handover (MIH) [15] and IEEE P1900.4 [16] architecture

## Slide 6: Evaluation of Bandwidth Estimation Approaches
use PCs equipped with IEEE 802.11 a/b/g Atheros 5212 chipset based wireless NICs which run on Linux OS with the open source MadWiFi WLAN driver [18]
AAC [6], ABE [7], and IAB [8]
RTS/CTS message exchanging is disabled
channel idle time, current transmission rate, and ACK timeout values are obtained by reading the specific information registers of Atheros HAL

## Slide 7: Transmission Counter Register
the amount of time spent for the frame transmission
while the load is increasing, the node spends more portion of the given time for the transmission

## Slide 8: Testbed and Parameters

## Slide 9: Effect of Different Measurement Period on the Correctness of the Bandwidth Estimation
the value of T directly affects the correctness of the estimated available bandwidth
  send 5 Mbps UDP traffic from one node, while estimating the available bandwidth by the second node

## Slide 10: Scenario without hidden/exposed nodes

## Slide 11: Scenario with hidden/exposed nodes

## Slide 12: Conclusion
proposed a new cognitive passive estimation of available bandwidth (cPEAB)
Passive measurement
open source MadWiFi WLAN driver
Compare with AAC, ABE, IAB, and Wbest
provide more accurate estimation in overlapped IEEE 802.11 WiFi WLANs

## Slide 13: Progress
Current
  Build ga client and server for screencasting
  Trying mark DSCP field for the video packets at server
Next
  Compare bandwidth estimation in GA to others
  Implement rate adaptation
GA Server
GA Client
Access point