## Slide 1: Programmatic Orchestration of WiFi Networks
Julius Schulz-Zander, Lalith Suresh, Nadi Sarrar, Anja Feldmann, Thomas Hühn, and Ruben Merz
2014 USENIX Annual Technical Conference

## Slide 2: Odin
An SDN framework for WiFi networks
Contributions:
  Light Virtual Access Points (LVAPs)
  A design and implementation for a software-defined WiFi network architecture based on LVAPs
  A prototype implementation on top of commodity AP hardware without modifications on clients

## Slide 3: Architecture of Odin

## Slide 4: LVAPs as Per-client APs
The association handshake with LVAP
  A client probe scans (probe request)
  A new LVAP spawned within Odin agent
  LVAP respond the probe request (probe response)
A physical AP hosts a unique LVAP for each connected client.
Notes: A client probe scans
A LVAP spawned within Odin agent
Probe respnse

## Slide 5: Processing path for WiFi frames

## Slide 6: State Encapsulated by LVAPs
LVAP comprises the following information:
  A unique virtual BSSID
  One or more SSIDs
  The IP address of the corresponding client
  A set of OpenFlow rules
Handoff:
  By migrating a client’s LVAP state from a physical AP to another to handoff a client without the client performing a re-association.
Notes: For every associated client, there is a corresponding LVAP
which comprises the following information

## Slide 7: Mobility Manager
The application collects the RSSI value from each client and maintains a map of each client’s RSSI value from the point of view of different agents.
It then assigns the clients to the agents where they can get the best RSSI value.

## Slide 8: Load Balancer
This application queries the framework once per minute to obtain the list of clients that can be seen by different APs and their corresponding RSSI values.
It uses this information to build a map of clients to lists of agents that are candidates for hosting their respective LVAPs. The application then evenly re-distributes LVAPs (clients) across physical APs, constrained by the hearing map.

## Slide 9: Automatic Channel Selection
It scans across all available channels and computes the average and the max RSSI for each channel center frequency. Based on multiple subsequent spectral scans, the ACS application picks the channel with the smallest maximum and average RSSI.
Notes: ACS algorithms aim at automatically determining the best available channel for a WiFi interface.

## Slide 10: Other Applications
Wireless troubleshooting
Energy Efficient WiFi Networks
Guest policy enforcement

## Slide 11: Progress update
Done:
  Patched SDN MPLS files to remove revisefilename.py
To-do:
  Try to run SDN MPLS experiment on real switch. (need to be confirmed)