## Slide 1: Programmatic Orchestration of WiFi Networks
Julius Schulz-Zander, Lalith Suresh, Nadi Sarrar, Anja Feldmann, Thomas Hühn, and Ruben Merz
2014 USENIX Annual Technical Conference
Notes: This paper presents the implementation of WiFi SDN. They introduced Odin as a framework, which has implemented six application on top of Odin.

## Slide 2: Introduction
Modern enterprise WiFi networks typically consist of few dozens to thousands of APs serving a multitude of client devices.
For performance and scalability reasons, these networks require some services for managing large scale networks.
These services have to be realized as applications on top of the basic management functionality of the individual APs.
Different devices from different vendors typically offer different interfaces and do not offer native support for the needed applications.
Notes: mobility management
load-balancing
interference management
channel reconfigurations
---

## Slide 3: Motivation
Need a novel abstraction/new tools to uniformly manage the wired and wireless network.
However, OpenFlow 1.0 can’t perform matching on wireless frames, report per-frame receiver side statistics ,etc.
Dyson, Flashback, DIRAC: require special software or hardware on the client.
Notes: Dyson: defining a set of APIs for clients and APs to be managed by a controller. The controller can query these nodes for channel information, form a global view of the network, and then control the network’s behavior to enforce a set of policies
Flashback: proposes a control channel technique for WiFi networks, by allowing stations to send short control messages concurrently with data transmissions
DIRAC: proposes a split-architecture wherein link-layer information is relayed by agents running on the APs to a central controller to improve network management decisions

## Slide 4: Odin
An SDN framework for WiFi networks
Contributions:
  Light Virtual Access Points (LVAPs)
  A design and implementation for a software-defined WiFi network architecture based on LVAPs
  A prototype implementation on top of commodity AP hardware without modifications on clients

## Slide 5: Architecture of Odin
OpenFlow protocol for wired network
Separate control plane protocol(Odin protocol) for programming the wireless part
Figure 1: High-level design of the Odin architecture.
Notes: We chose to have separate protocols for programming the wired and wireless parts.

## Slide 6: Light Virtual Access Point (LVAP)
LVAP is an abstraction
As a per-client APs
State encapsulation
Slicing and control logic isolation
Multi-channel operation
Supporting authentication
Notes: Multi-channel operation: For multichannel operation, Odin can leverage IEEE 802.11h (restricted to 5GHz band) to instruct clients to switch to a different channel while keeping association state intact.
Support WPA2 and Guest WiFi.
WAP2: LVAP will store the session key in LVAP state.
Guest WiFi: similar to most universities do.

## Slide 7: LVAPs as Per-client APs
In regular IEEE 802.11 network, client decides which AP to associate with via a locally made choice.
Problem: there is no mechanism for centralized control over the client’s association.
Dyson, which introduced additional signaling techniques.
Notes: Dyson: the infrastructure cannot instruct the client to re-associate without introducing additional signaling techniques.

## Slide 8: Processing path for WiFi frames
Figure 2: Processing path for WiFi frames:
Agents invoke a controller for handling management frames.
Notes: Probe request
LVAP spawned
The LVAP send probe response

## Slide 9: State Encapsulated by LVAPs
Physical Access Point
Figure 3: Per-Client LVAP state: a unique BSSID, set of SSIDs, client’s IPv4 address, and OpenFlow rules (80 bytes of state excluding OF rules)

## Slide 10: Slicing and Control Logic Isolation
Figure 4: Odin applications operate upon a view of LVAPs and physical APs in their respective slices.
Notes: Accommodating multiple logical networks on top of the same physical infrastructure with different policies and control applications is called network slicing.
When clients attempt to associate to a particular SSID, they are automatically assigned to the slice to which the SSID belongs.
An application is only presented a view of the network corresponding to its slice.

## Slide 11: Reactive and Proactive Application
Measurements from the agent:
  Reactive applications make use of a publish-subscribe system of the Odin agent.
  Application can register thresholds for Rx-statistics, like RSSI, bit-rate, timestamp of the last received packet.
OpenFlow statistics
  Applications can query through controller to make traffic-aware routing decisions.
External measurement sources
  CPU and memory utilization, channel active/busy times.
Notes: … in order to have a handler invoked at the application whenever a per-frame event of interest occurs at the agents.
As above.
applications can access data from multiple measurement sources outside the Odin framework, including the CPU and memory utilization and the channel active/busy times collected by tools such as collectd.

## Slide 12: Mobility Manager
The application collects the RSSI value from each client and maintains a map of each client’s RSSI value from the point of view of different agents.
It assigns the clients to the agents where they can get the best RSSI value.

## Slide 13: Load Balancer
This application queries the framework once per minute to obtain the list of clients that can be seen by different APs and their corresponding RSSI values.
It uses this information to build a map of clients to lists of agents that are candidates for hosting their respective LVAPs. The application then evenly re-distributes LVAPs (clients) across physical APs, constrained by the hearing map.

## Slide 14: Load Balancer
Notes: We observe an increase in fairness among clients with load balancing enabled:
i.e., roughly 50% of the clients were able to transmit around 20 MB of data with load balancing enabled compared to 15% without load-balancing.

## Slide 15: Automatic Channel Selection
It scans across all available channels and computes the average and the max RSSI for each channel center frequency. Based on multiple subsequent spectral scans, the ACS application picks the channel with the smallest maximum and average RSSI.
Notes: ACS algorithms aim at automatically determining the best available channel for a WiFi interface.

## Slide 16: Automatic Channel Selection

## Slide 17: Other Applications
Wireless troubleshooting
Energy Efficient WiFi Networks
Guest policy enforcement

## Slide 18: Controller load due to Pub-Sub
Figure 11: Normalized CPU utilization (2-cores) on the controller per density factor.
bottlenecked
Notes: 9 APs, use load generator by Remote Procedure Call (RPC) to mock client.
---
An increase in the number of clients for a fixed density factor leads to an increase in the controller’s CPU utilization.
for a fixed number of clients, an increase in the density factor leads to an increased number of the mobility manager’s subscriptions being triggered.

## Slide 19: Comparison of Handoffs
Figure 12: Impact of a LVAP migration andWiFi handoff on TCP throughput.
Notes: With Odin’s LVAP handoff, the TCP throughput is unaffected.
As Figure 12 indicates, there is an overall reduction of throughput (close to 5 Mbit/sec) with Odin as opposed to regular WiFi.
This is, because we currently use userspace Click to run the Odin agents, resulting in slower and jittery forwarding performance on our APs which makes TCP to throttle down.

## Slide 20: LVAP-Handoff frequency benchmark
Figure 13:
TCP throughput during Odin LVAP-handoffs.
Notes: a single iperf-based TCP flow is executed
30s, 5s – 25s handoff
---
LVAP-based handoffs are leading to no significant throughput degradation of the TCP flow.

## Slide 21: Probe request serving latency
Table 2: Latency for serving probe requests (excluding transmission time on the channel) across 9 APs

## Slide 22: Conclusion
Through the LVAP abstraction, Odin is well suited to address the complexities of the IEEE 802.11 protocol.
Odin runs on top of today’s commodity access point hardware without requiring client modifications.
They present one promising way to uniformly manage both wired and WiFi networks.

## Slide 23: Progress update
Done:
  Install Click on OpenWrt (haven’t patched ath9k driver)
To-do:
  Prepare SDN monthly report by end of today
  Patch ath9k driver
  Enable Odin agent
  Connect Odin agent and master