## Slide 1: First Person Omnidirectional Video: System Design and Implications for Immersive Experience
TVX 2015

## Slide 2: Introduction
Recording and sharing own experience completely has been an ultimate goal of media technology
Omni-Directional Video (ODV)
  Capturing, displaying, interaction and control interface
First person Omni-Directional Video (FODV) play important role in various applications
  E.g., entertainment, sports viewing, education and simulation training, news casting and therapy

## Slide 3: Difficulties
Design of capturing device for FODV
  wearable omnidirectional camera attached to the head
  no existing solution to satisfy all of robustness, wearability and eye-level position
Quality of the first-person video from wearable cameras
  often shaky due to the body movement during capturing → viewers often feel dizzy
  gets worse when the visual experience is immersive on a large screen or HMD
  Cybersickness

## Slide 4: Contributions
System design including capturing device and image processing for stabilizing FODV
An investigation of cybersickness and user experience of the system
Design implications for FODV from series of demo and workshop with their proposed FODV system

## Slide 5: System Design
JackIn Head system
  headgear with multiple cameras to capture omnidirectional video
  image processing for FODV stabilization
  the streaming video data and a playback system with screen or HMD

## Slide 6: Headgear with Omnidirectional Camera
Design considerations
  lower center of balance
  Captured environment should be close to the first person viewpoint
Existing USB camera module has limitation in terms of image quality and video frame rate
Each camera capture 960x1440 pixel, 100 fps

## Slide 7: Image Stabilization for First Person ODV
Calculates rotation then eliminate its rotation
Re-produce smoothed rotation to follow the wears head direction with variable parameter
Parameter depends on video context
  zero or quite small → independent view (intense motion)
  larger value → smoothed view (daily activities)

## Slide 8: Image Stabilization for First Person ODV
Calculates rotation then eliminate its rotation
Re-produce smoothed rotation to follow the wears head direction with variable parameter
Parameter
  parameter is zero or quite small → independent view
  parameter is larger value → smoothed view

## Slide 9: Evaluation of Cybersickness
Scenarios
  Scenario (A): Walking in the town
  Scenario (B): Ball sports, watching to trace the ball
  Scenario (C): Ball sports, watching to trace another player

## Slide 10: Experiment setup
Participants perform six tasks in total (non-stabilization/stablization)
  A-N, A-S, B-N, B-S, C-N, C-S
Each task is two minutes with a recovery time of 30 minutes interval
Before and after each task, filled out a simulator sickness questionnaire (SSQ)
  the degree to which the participant felt nausea, oculomotor discomfort, disorientation, and general cybersickness
12 volunteers aged 20-38

## Slide 11: Experiment Results
The stabilization lessened the instances of cybersickness in each scenario
There was a significant difference, between A-N and A-S, also between C-N and C-S

## Slide 12: Analyses and Observations
Active viewing behavior or not
  Without stabilization, strong disorientation when sudden motion in the direction opposite to their intention occurred (A, C)
  Stabilization would be a beneficial feature in FODV application
Synchronization and asyncronization
  synchronization in motion of FODV and the spectator will lead lessen cybersickness, and also produce more realistic sensations (B)

## Slide 13: Analyses and Observations (cont.)
Existence of first person
  head direction is an important indication of awareness, and was eliminated by stabilization
  visualization of the wearer’s head direction in the immersive view can address this problem
Cybersickness induced by translational movement even after stabilization
  the viewer expects to experience acceleration from the visual motion caused temporal cybersickness
  vertical translational motion, which cannot be eliminated by current stabilization process

## Slide 14: Setup of Workshop
50 people
HMD with head tracking and 15 inch laptop screen
Activities
  Virtual travel: realistic feeling, revisit
  Virtual gymnastics: with vs. without gymnastics experience
  Virtual flying experience of the paraglider: virtual tutorial

## Slide 15: Technical Challenges
headgear should be less weighted and more suitable for wear, and even flexible form factor
The stabilization should be improved in terms of compensating for the translational acceleration and vibration noise
Visual gaps in the omnidirectional image also should be addressed
Realtime

## Slide 16: Technical Challenges
headgear should be less weighted and more suitable for wear, and even flexible form factor
The stabilization should be improved in terms of compensating for the translational acceleration and vibration noise
Realtime

## Slide 17: Design Implications
The risk of cybersickness even with footage of walking activities → stabilization
Overlaying ego-motion of the wearer in omnidirectional video will help the spectator to understand what the wearer was watching and doing

## Slide 18: Design Implications
The risk of cybersickness even with footage of walking activities → stabilization
Overlaying ego-motion of the wearer in omnidirectional video will help the spectator to understand what the wearer was watching and doing
Design space for first person omnidirectional video viewing
  what kind of user experience is expected, how stabilization should be applied and what other implementation matters

## Slide 19: Design Implications (cont.)
Synchronization of motion will lessen the induction of cybersickness, but also will produce an immersive realistic sensation
  adaptive control of stabilization will be one of possible application to increase immersion
Viewing angle information of spectators
  The collected date of those information will generate meaningful information about social interest in ODV

## Slide 20: Conclusion
Omnidirectional video is one of promising media and have capability to capture an immersive first person experience
Aimed to provide a solution for existing problems and to explore design implications
  Capturing device and image stabilization to alleviate cybersickness
  Evaluating and summarized the findings and insight into design implications
Contribute a further exploration of first person omnidirectional video and expand the eco-system of interactive experience of various media

## Slide 21: Related Work
User experience in omnidirectional video
Omnidirectional camera
Cybersickness
Omnidirectional image processing and stabilization

## Slide 22: Design parameter
Wider FOV wearable camera will reduce number of camera → reduce the visual gap in stitched omnidirectional video
longer shutter speed or lower frame rate produce image blur which cause error in stabilization
Stitching multiple lower frame rate videos generates not only visual gap, but also unexpected jitter through the stabilization process

## Slide 23: Image Stabilization for First Person ODV (cont.)
In each equirectangular video frame I(t), image feature points pn(t) are extracted by finding the visual corner in the equirectangular image
pyramidal KLT tp calculate optical flow fn(t) → pn(t + 1) = pn(t) + fn(t)
2-D image feature points → 3-D points