## Slide 1: A Survey Of Distributed Video Coding
NTHU NMSL
Shu-Ting Wang
2012/12

## Slide 2: Abstract
Introduction
System Framework
  DISCOVER Codecs
  Recent Research and Future work

## Slide 3: Abstract
Introduction
System Framework
DISCOVER Codecs
Recent Research and Future work

## Slide 4: Which Theories?
Slepian and Wolf for lossless distributed source coding
Wyner and Ziv for the lossy distributed source coding

## Slide 5: Basics(1/4)
the rate-distortion performance achieved when performing joint encoding and decoding of two correlated sources can also be obtained by doing separate encoding and joint decoding

## Slide 6: Basics(2/4)
the sum of rates,, can achieve
the joint entropy H ( X, Y ), just as for joint
encoding of X and Y , despite separate encoders
for X and Y .
Notes: Consider two statistically dependent i.i.d. ﬁnite-alphabet
random sequences X and Y . With separate conventional
entropy encoders and decoders one can achieve RX H ( X )
and RY H ( Y ), where H ( X ) and H ( Y ) are the entropies
of X and Y , respectively

## Slide 7: Basics(3/4)
The source produces a sequence X with statistics that depend on side information Y which improve decoding.
Notes: Since RY = H ( Y ) is achievable for (conventionally)
encoding Y , compression with receiver side information cor-
responds to one of the corners of the rate region in Fig. 2, and
hence RX >=H ( X | Y ), regardless of the encoder’s access to
side information Y .

## Slide 8: Basics(4/4)
We are interested in the case where Y is available at the decoder, but not at the decoder.

## Slide 9: Abstract
Introduction
System Framework
DISCOVER Codecs
Recent Research and Future work

## Slide 10: Early Architectures
Two kinds of architecture
  PRISM
  Stanford
Nowadays, state-of-the-art codecs are based on Stanford architecture because of its efficiency.

## Slide 11: PRISM Architecture

## Slide 12: Stanford Architecture

## Slide 13: Overview

## Slide 14: Road Map

## Slide 15: Frame Splitting
Input frames are split into two parts
  Key Frames
  Wyner-Ziv Frames
Key frames are
  coded by MPEG/H.264 intra
  to prevent error drifting problem

## Slide 16: Road Map

## Slide 17: Discrete Cosine Transform(1/2)
DCT has good energy compaction property and human eyes can hardly perceive the high frequency bands.
The transform-domain DVC codec has shown
its better R-D performance than the pixel-
domain one

## Slide 18: Discrete Cosine Transform(2/2)

## Slide 19: Road Map

## Slide 20: Quantization(1/3)
Sampled signal
Quantized signal
Digital signal (sampled, quantized)

## Slide 21: Quantization(2/3)
Q table is simple for implementation, it cannot keep the coding quality on various video sequences.
Stanford-based DVC codecs have the Q table for quantization like traditional video codecs

## Slide 22: Quantization(3/3)
PRISM employing the classiﬁcation method
  Low correlation : use conventional coding
  High correlation: skip
  Other: distributed coding

## Slide 23: Road Map

## Slide 24: Encoder
PRISM codec do more on encoder to achieve better rate-distortion performance.
Encoder can generate hash code for decoder (hash-based motion estimation) to choose better side information.

## Slide 25: Road Map

## Slide 26: Channel Coding(1/2)
Turbo code or LDPC code are usually used to encode the quantized bands bit-plane by bit-plane.
Parity bitstreams (or syndrome bits) are kept in the buffer.
Rate estimator will determine how many parity bits to be sent to the decoder.

## Slide 27: Channel Coding(2/2)
Cyclic Redundancy Check (CRC) is used to verify the correctness of the decoded bands.
Obvious disadvantage: the iterative decoding process cause significant delay.
Many research are focus on rate estimation and reducing the number of feedback

## Slide 28: Road Map

## Slide 29: Side Information
The key operation of the side information generation is motion-compensated frame interpolation or hash-based motion estimation , where true motion ﬁeld is required to get the best quality.
The quality of Wyner-Ziv frames is strongly determined by the the side information.

## Slide 30: Road Map

## Slide 31: Correlation Noise Modeling(1/2)
DVC systems usually use Laplacian distribution to model the bit conditional probability of bit-planes for decoding.
Notes: 由於它可以看作是兩個不同位置的指數分布背靠背拼接在一起，所以它也叫作雙指數分布。兩個相互獨立同機率分布指數隨機變數之間的差別是按照指數分布的隨機時間布朗運動

## Slide 32: Correlation Noise Modeling(2/2)
A good correlation noise model leads to better
R-D performance. Early methods are offline
training methods.
Online modeling and TRACE( transfrom- domain adaptive correlation estimation) are purposed to improve the modeling algorithm.

## Slide 33: Road Map

## Slide 34: Reconstruction and Post-processing
The minimum min square error (MMSE) method and Inverse DCT are applied to get the optimal decoded frames.
The deblocking filter technique in traditional codec can be adopted to DVC system.

## Slide 35: Abstract
Introduction
System Framework
DISCOVER Codecs
Recent Research and Future work

## Slide 36: DISCOVER architecture

## Slide 37: DISCOVER RoadMap

## Slide 38: Frame Splitting
For the DISCOVER codec, an adaptive Group of Picture (GOP)size selection module was developed to control the (non-periodic) insertion of key frames in between the WZ frames.

## Slide 39: DISCOVER RoadMap

## Slide 40: Channel Encoder and Buffer(1/2)
The LDPCA codes are better than the turbo codes at the capacity of many communication channels, including the virtual channel in DVC.
An LDPCA encoder consists of
  LDPC syndrome-former
  accumulator
If the decoder fails, more accumulated syndromes are requested from the encoder buffer using a feedback channel.

## Slide 41: Channel Encoder and Buffer(2/2)
If the decoder fails, more accumulated syndromes are requested from the encoder buffer using a feedback channel.

## Slide 42: DISCOVER RoadMap

## Slide 43: Frame Interpolation Framework(1/5)
Interpolated
frames
Forward Motion
Estimation
Bi-Directional
Motion
Estimation
Bi-Directional
Motion
Compensation
Spatial Smoothing
Low pass filter
Low pass filter
Motion Vector
Previous
Key frames
Next
Key frames

## Slide 44: Forward Motion Estimation(2/5)
Forward Motion Estimation ,the rigid block based motion estimation scheme, fails to capture all aspects of the motion field
Once the frame interpolation is performed, overlapped and uncovered areas will appear.
Notes: This is because the motion vectors obtained do not necessarily intercept the interpolated frame at the center of each non-overlapped block in the interpolated frame.

## Slide 45: Bi-Directional Motion Estimation(3/5)
This motion estimation technique selects a linear trajectory between the next and previous key frames passing at the center of the blocks in the interpolated frame.
Notes: i.e. (x1 , y1 ) = (xi , yi ) + MV(B i ) and (x2 , y2 ) = (xi , yi ) -
MV(B i ), where (x1 , y1 ) is the coordinates of the block in the previous key frame, (x2 , y2 ) are the coordinates
of the block in the next frame and MV(B i ) represents the motion vector obtained in the previous section
divided by half, since the interpolated frame is equally distant to both key frames.

## Slide 46: Spatial Smoothing(4/5)
Sometimes the motion vectors have low spatial coherence.
This can be improved by weighted vector median filters, which maintains the motion field spatial coherence by looking for candidate motion vectors at neighboring blocks at each block.

## Slide 47: Bi-Directional Motion Compensation(5/5)
When final motion vector field is obtained, the interpolated frame can be filled by using bidirectional motion compensation as defined in standard video coding schemes.

## Slide 48: DISCOVER RoadMap

## Slide 49: Virtual Channel Model & Soft Input Calculation
The DISCOVER codec uses a Laplacian distribution to model the correlation noise, i.e. the error distribution between corresponding DCT bands of SI and WZ frames.
The DISCOVER codec estimate the Laplacian distribution parameter α at the DCT band level and at the coefficient level.

## Slide 50: DISCOVER RoadMap

## Slide 51: Reconstruction and Inverse Transform
The decoded value is reconstructed in a mean squared error-optimal way as the expectation of x given the decoded quantization index q .
The side information value:
Finally, the inverse 4x4 DCT is applied to restore the Wyner-Ziv frames to pixel domain.

## Slide 52: DISCOVER Performance

## Slide 53: Abstract
Introduction
System Framework
DISCOVER Codecs
Recent Research and Future work

## Slide 54: Recent Research
Recent research are focus on
  Side information: frame interpolation technique
  Correlation noise modeling
  Fast decoding : Using GPU to speed up decoding
  New codec architecture: VISNET II DVC codec by some people who develop DISCOVER codec
  distributed compressive video sensing (DCVS) is to simultaneously capture and compress video data

## Slide 55: Future Work
Distributed video streaming
Wireless low-power surveillance
Visual sensor networks