## Slide 1: CloudMAC - An OpenFlow based Architecture for 802.11 MAC Layer Processing in the Cloud
Peter Dely, Jonathan Vestin, Andreas Kassler, Computer Science Department Karlstad University Nico Bayer, Hans Einsiedler, Christoph Peylo, Telekom Innovation Laboratories, Berlin, Germany
GC'12 Workshop: The 8th Broadband Wireless Access Workshop
Notes: partially offloading the MAC layer processing to virtual machines provided by cloud services
In Cloud- MAC APs just forward MAC frames between virtual APs and IEEE 802.11 stations

## Slide 2: Introduction
Current WLAN management protocols
  CAPWAP, LWAPP
  Use a centralized controller to discover APs, configure them and provide authentication and authorization services to mobile clients
Hard to extent with new functionality
CloudMAC
  The processing of MAC data/management frames is implemented in in cloud
  APs just forward MAC frames
Notes: However, this would make the network become too complicated to management when scale increased
In CAPWAP, the state of the connection is shared between controller and the AP

## Slide 3: CloudMAC
A distributed architecture in which 802.11 WLAN MAC processing is partially performed in cloud
Architecture:
VAP
WTP
Notes: complete MAC layer is located at the local AP

## Slide 4: CloudMAC – Virtual APs
Virtual APs (VAPs)
  OS instances running on a virtualization host
  Each VAP has one or several virtual WLAN cards
    Connect to physical cards on different WTPs
  Run access point management software,
    generate beacon frames
    respond to association/authentication MAC frames
Notes: A virtual WLAN card is a driver that appears to the OS and user space applications like a normal physical WLAN card
So the standard software such as Hostapd can be deployed as the VAPs

## Slide 5: CloudMAC – Wireless Terminal Point
Wireless Terminal Points (WTPs)
  Slim APs with WLAN cards allow to send and receive raw MAC frames
  Generate frames with hard-real time constraints (ACKs and frame retransmissions)
WTPs and VAPs are connected with each other via layer 2 tunnels and an OpenFlow switch
Notes: The virtual WLAN card in the VAP generates MAC frames, then adds control headers and encrypts the frames
Then the WTPs transmit those frames to the stations

## Slide 6: CloudMAC – OpenFlow Switch
OpenFlow Switch
  Switch table specifies what frames to forward to which WTP or VAP
  The table represents the binding between VAPs (virtual WLAN cards) and WTPs
Notes: So the AP can easily be moved from one WTP to another by reconfiguring the switch table
OpenFlow implementation such as OpenvSwitch allows to re-write the control header information
As each physical card on a WTP can be bound to multiple virtual WLAN cards (traffic can be distinguished by the BSSID and MAC addresses)

## Slide 7: CloudMAC Implementation
KAUMesh testbed [10]
WTPs
  Cambria GW2358-4 embedded devices with Atheros chipset
  OpenWrt Backfire, ATH5K as WLAN driver
VAPs
  Debian 6.0 VMs
  Use hostapd to generate beacon message and provide authentication and authorization services
  Virtual WLAN card driver is based on the mac80211_hwsim driver, they modified it to allow reading and injecting raw IEEE 802.11 frames
P.DelyandA.Kassler,“KAUMeshDemo,”in Proc.of 9th Scandinavian Workshop on Wireless Ad-hoc and Sensor Networks, 2009.
Notes: which is a software simulator of an IEEE 802.11 device used for testing MAC functionality and user space tools such as hostapd

## Slide 8: CloudMAC Implementation (cont’d)
Packets between the VAP, the switch and the WTP are tunneled using the Capsulator
OF Switch
  Open vSwitch 1.3.0
Notes: Capsulator is a user-space program which can be used to transparently connect networks. In particular, it can make an arbitrary number of links act as if they were connected to a hub.

## Slide 9: Performance Evaluation
Comparison
  Normal WLAN AP
Metrics
  RTT
  TCP throughput between a station and the VAP/IP router

## Slide 10: Evaluation - RTT
RTT increases because of the additional processing at the OpenFlow switch and due to delay added by the tunnels
The time for whole association procedure was similar on both systems (~1.44 sec)
Notes: But they said that in their experiment, the critical MAC frames liks association response message are delivered fast enough to have the normal operation

## Slide 11: Evaluation - Throughput
Throughput is decreased slightly due to the additional components added by CloudMAC
Their current tunneling implementation runs in user space and require context switching
Notes: The performance can be improved by using the kernel-space tunnels

## Slide 12: Case Study – Seamless AP Switch-off System
To save energy by switching off some APs/WTPs that cover overlapping area if the network load is low
STA runs Linux and uses wpa_supplicant to find networks and associate to them
Comparison
  Normal WLAN AP
Metrics
  Number of lost packets
  TCP sequence-time
Notes: In this test scenario, there are to WTP. The station first connect to WTP1, In the test of cloudMAC, the directly modify the flow table in OpenFlow switch to transfer the traffic from WTP1 to WPT2.
In the test of normal WLAN, they let the WTP1 to send a disassociation message to the STA and then switch off the WTP1.
Hence, the station needs to find a new AP and then connect to the WTP2.

## Slide 13: Evaluation – AP Switch
Send UDP datagrams from external server to STA
With CloudMAC on average 3.5 packets are lost during the switch
Notes: In the test of normal WLAN, it lose lots of packets when switch the AP

## Slide 14: Evaluation – AP Switch
TCP download
The time/sequence graph of CloudMAC is smooth and steady
Notes: In the normal WLAN, there is no throughput between second 3 and 30
During that time, the link layer connection needs to be re-established

## Slide 15: Comparison
Differ from Odin in the way association states are handled
  Odin keeps the state in the agents on APs and controller
  CloudMAC doesn’t need to manage association states on physical APs

## Slide 16: Conclusion
CloudMAC, a WLAN management architecture that most processing and management functionality is on VAP
CloudMAC APs are simple devices that relay MAC frames between VAPs and mobile stations via an OpenFlow controlled network