## Slide 1: On Scalability of Software-Defined Networking
S.H. Yeganeh, A. Tootoonchian, Y. Ganjali
University of Tronto
IEEE Communication Magazine

## Slide 2: Motivations
There have always been concerns about performance and scalability about SDN
Argue that there is no inherent bottleneck to SDN scalability
  Often came from implicit and extrinsic assumption
  These problems are also faced by traditional networks
  If carefully implemented, these problems can be avoided, ex: implemented as distributed system

## Slide 3: Discussed Scalability Issue
Scalability of controller (major)
Flow Setup overhead
Resilience to failures

## Slide 4: Controller Scalability
Early benchmark of NOX
  Only handle 30K requests while maintaining a reasonable flow install time (sub-10ms)
Two way to solve this problem
  Improve the parallelism, improve IO performance
  Implement as distributed system

## Slide 5: Controller Scalability
Improve the parallelism, improve IO performance
  Parallel version of NOX (HOT-ICE 2012)
  DIFANE (SIGCOMM 2010)
  DevoFlow (SIGCOMM 2011)
Implement as distributed system
  Onix (OSDI 2010)
  HyperFlow (INM/WREN 2010)
  Kandoo (HotSDN 2012)

## Slide 6: Flow Initiation Overhead
Early design such as Ethane and NOX makes people think flows have to be reactive
  This is not true
Two possible way
  Aggregate rules
  Proactively install rules
DIFANE in some way did this

## Slide 7: Resiliency To Failures

## Slide 8: Resiliency To Failures
Early design use only one centralized controller
  This doesn’t have to be the case
Link failure notification
  Traditional: flooded across the network
  SDN: switch to controller (info propagation delay is no worse, and a controller dedicated to deal with the problem)
Not worse than traditional network
  Similar techniques can be applied, ex: preprogrammed backup paths

## Slide 9: Scalability In Different Settings
Data Centers
  Large number of devices, controller will be overload
    Use proactive install rules but sacrifice precision and reactivity
    Use distributed system if those can’t be sacrifice
Service Provider Networks
  Geographically distributed, worsen the latency issue
    Partition into regions
  High number of flows
    Aggregated rules

## Slide 10: Other Topic
Behavioral and Programming Abstractions
  Ease of management
Testing and Verification
  Ease of troubleshooting
Extensibility
  How to support more protocols

## Slide 11: Conclusion
Argue the scalability concern
  Are neither caused by nor fundamentally unique to SDN
  Can be addressed without losing the benefit of SDN
Emphasize the potential gain on other topics