## Slide 1: FlexCast: Graceful Wireless Video Streaming
S. Aditya & Sachin Katti
Stanford University

## Slide 2: Outline
Background
Introduction
Algorithm
Experiment
Conclusion
Reference

## Slide 3: Background

## Slide 4: Mobile Video Streaming
buffering, lost frames are quite common

## Slide 5: Why is Performance Choppy?
Current video streaming (MPEG4..)
  Encode video at a specific bitrate (e.g 1mbps+ for HD)
  Expect wireless network to deliver that reliable bitrate
Wireless Networks
  Do not guarantee a specific minimum reliable bitrate

## Slide 6: Introduction

## Slide 7: FlexCast
Reconstructs a video even from erroneous packets with quality commensurate with current network quality
Key High Level Principle: Bit Errors in packets should translate proportionally into distortion errors in video
  Entropy Coding does not have that property, a few bit errors can completely distort decoded video
  Flexcast eliminates entropy coding, uses soft reconstruction and proportional representation to achieve proportionality

## Slide 8: Key Insight 1: Soft Reconstruction
PHYs compute soft estimates of decoded bits  probability bit is “1” or “0”
  Soft Output Viterbi Decoder, SoftPHY
Leverage soft information to compute expected value of DCT coefficient

## Slide 9: Soft Reconstruction
Soft Reconstructed DCT coefficient (9.1) is much closer to the transmitted value than traditional (6)

## Slide 10: Key Insight 2: Proportional Representation
Soft Reconstruction is not sufficient since some bits are more important than others
  MSB of the low frequency DCT coefficient, single bit error translates to large video distortion
Second Principle: Design a technique that allows sender to provide unequal error protection (UEP) without modifying the PHY

## Slide 11: Algorithm

## Slide 12: Low-density parity-check code ( LDPC )
LDPC
  Low-density parity-check codes
  Error correct codes
  Low density give a low complexity
  N inputs produce r check point
  Ex: N=10 r=5

## Slide 13: Low-density parity-check code ( LDPC )
1
1
0
1
0
1
1
0
0
0
0
0
Encode
Decode
1
?
0
?
0
?
1
0
0
0
0
0

## Slide 14: LT Codes
d
v
2
(101000)
2
(110000)
2
(000011)
2
(000101)
1
(010000)
1
(000010)
3
(100101)
1
(001000)
1
(001000)
1
(000100)
Bit Node
Check Node

## Slide 15: Distortion Grouping
Identify how important groups of bits are by estimating the amount of distortion they would cause if decoded in error

## Slide 16: Rateless Code for UEP
To provide UEP, sender encodes each distortion group with a rateless Raptor code

## Slide 17: Soft Raptor Decoder
• PHY passes demodulated bits with soft information
• Apply Belief Propagation to decode Raptor Code and compute soft estimate for the DCT coefficient bits

## Slide 18: Soft Raptor Decoder
General case
Conflict case

## Slide 19: FlexCast Architecture

## Slide 20: Experiment

## Slide 21: Implementation
FlexCast is implemented by modifying standard MPEG4 implementation
Algorithms have linear complexity and are practical to implement

## Slide 22: Evaluation Setup
Deployed in an 10 node indoor USRP2 testbed
PHY: WiFi style OFDM, 6.25 MHz channel
Standard WiFi convolutional coding rates

## Slide 23: How Graceful is FlexCast?
FlexCast performs as well as the omniscient scheme without requiring any channel state knowledge

## Slide 24: Trace Driven Emulation
Stanford RUSK channel sounder
  High precision channel measurement
  Continuous channel state information
2.426 GHz to 2.448 GHz (WiFi channel 6)
Each trace: 100000 measurements over 100 sec
10 mobility traces at walking speed ~ 3 mph
Simulate mobility by playing trace at increasing speeds

## Slide 25: Performance with Increasing Mobility
FlexCast provides near optimal performance at high mobility

## Slide 26: Conclusion
FlexCast provides graceful video streaming for dynamically varying wireless networks
Espouses a design philosophy that takes into account wireless channel properties to build modular robust protocols and systems

## Slide 27: Reference
FlexCast: Graceful Wireless Video Streaming, S. Aditya and S. Katti, Mobicom'11
FlexCast Slide
  http://www.sigmobile.org/mobicom/2011/slides/254-flexcast-slides.pdf
Raptor Codes
  http://vod.cs.nthu.edu.tw/ezLMS/show.php?id=341&1313668771