## Slide 1: End-to-end congestion control approaches for high throughput and low delay in 4G/5G cellular networks

## Slide 2: Introduction
5G Cellular Networks
  Enhanced Mobile Broadband (eMBB)
    3D and Ultra High Definition (UHD) videos
    Cloud Gaming
    Augmented Reality
  Ultra Reliable and Low Latency Communications (URLLC)
    Self-driving Cars
    Industrial Automation
  Massive Machine-type Communications (mMTC)
    Sensor Networks
    Smart City
    Home Applications

## Slide 3: Introduction
Common congestion control algorithms (CCAs)
  Packet loss as a congestion signal
  Queuing delay (bufferbloat)
New cellular CCAs are developed under two main assumption:
  Content moving closer to the cellular access link
    reduce the cost of transferring across expensive long-haul links (WANs)
    make the radio link become the bottleneck
  Reduced cross-traffic effect due to per-user queues
    Place different users flows in separate queues

## Slide 4: Related Work

## Slide 5: The potential impact of 4G/5G technologies and use cases on congestion control
Link adaptation
  An evolved Node B (eNodeB) selects the modulation and coding scheme to be used in the communication based on the reported signal quality
mmWave
  Higher data rates
  High propagation loss
  Easily affected by blocking entities
Small cells
  Increase capacity
  Increase the scale and number of load variations
  Increase the handovers and state reconfigurations frequency

## Slide 6: The potential impact of 4G/5G technologies and use cases on congestion control
MIMO (Multiple Input Multiple Output)
  Enable multiple antenna transmissions
  Higher data rates and/or better transmission reliability
Carrier aggregation
  Use multiple carriers simultaneously to obtain a larger bandwidth for transmission
  Primary component carrier (PCC) - only changed during handovers
  Secondary component carriers (SCC)

## Slide 7: The potential impact of 4G/5G technologies and use cases on congestion control
Dual connectivity (DC)
  Connect to two access networks at the same time
  Higher peak data rate
  High fluctuations in data rate
Dynamic network slicing and resource allocation
  Network slicing - divide the physical network infrastructure into multiple separate logical network entities
  Dynamic resource allocation
Converged heterogeneous services
  Could add extra delay

## Slide 8: Conventional end-to-end congestion control in current cellular networks
End-to-end congestion control in the Internet
  In transport layer – TCP, QUIC, SCTP
  Outside transport layer - Real time media streaming (on UDP)
  Loss or delay for detecting congestion
  Additive increase multiplicative degrease (AIMD)
  Slow-start
    Start from an initial value and double the congestion window (CWND) every round-trip time (RTT) until its threshold (ssthresh) is reached or a packet loss is experienced
  Congestion avoidance
    TCP NewReno : sets the ssthresh to half the latest CWND and update the CWND to the ssthresh value
    TCP CUBIC : records the current CWND as the maximum window size(Wmax), then decreases its CWND to a value determined by a multiplicative decrease factor

## Slide 9: Conventional end-to-end congestion control in current cellular networks
Congestion control issues and in-network solutions in cellular networks
  Network access layer issues and solutions
    Non-congestion packet loss
    Radio link control (RLC) and medium access control (MAC)
      Hide the random packet losses from the data sender
  Internet layer issues and solutions
    The large buffers delay the detection of congestion at the end nodes
    Active queue management (AQM)
  Multi-layer solutions
    Performance enhancing proxies (PEPs)

## Slide 10: Challenges in designing new end-to-end CCAs for cellular networks
Avoiding underutilization in an environment with high bandwidth variability.
Achieving full utilization without creating large queueing delays in the large buffers provided to improve the utilization of the highly variable capacity by popular loss-based CCAs.
Being able to differentiate between delay variations caused by traffic competition and delay variations caused by radio channel events, e.g., interference, multi-path fading, etc.

## Slide 11: Challenges in designing new end-to-end CCAs for cellular networks
Tracking the highly variable bandwidth
  probing
Avoiding large queueing delay
  Large buffers
Insensitivity to non-queuing delay variability
  Wrong congestion decision

## Slide 12: Classification of CCAs for cellular access

## Slide 13: Classification of CCAs for cellular access
Reactive algorithms
Predictive algorithms
Network-assisted algorithms

## Slide 14: Reactive algorithms

## Slide 15: Predictive algorithms

## Slide 16: Network-assisted algorithms

## Slide 17: Deployment factors
Downlink/uplink asymmetry
Specificity of design
Required modifications
TCP friendliness
Performance tradeoff
Cross-layer dependency

## Slide 19: Opportunities and outstanding issues
Integration and interaction with SDN/NFV
Leveraging edge/fog computing and ICN
High utilization as the peak rate and variability increases
Improving fairness between flows
  Applying multi-domain congestion control
  Minimizing flow interactions
Evaluating CCAs through independent testing and benchmarking

## Slide 20: Summary and conclusions
Focus on transport-layer, end-to-end algorithms
Three broad groups of CCAs
Future works